## Slide 1: OPTIMIZING JOB SHOP SCHEDULING WITH DEEP REINFORCEMENT LEARNING
Prof. Hamidreza Heidari

## Slide 2
Group Members :
Sanaboyina Satya Narasimha
Rifshu Hussain Shaik
Gnanasudha Patur
Alwin Shaji
Ankith Ramesh Babu

## Slide 3: Introduction
This project applies Deep Reinforcement Learning (DRL) to optimize the Job Shop Scheduling Problem (JSSP).
It enables real-time, adaptive scheduling that improves makespan, machine utilization, and job tardiness.
The goal is to enhance efficiency and adaptability in smart manufacturing systems.

## Slide 4: The Real Industrial Problem
Dynamic Production Environments
Real factories experience machine failures, tool changes, random job arrivals, and urgent customer orders, making static schedules quickly outdated.
FIFO and SPT can balance fairness and efficiency — FIFO ensures orderly job flow, while SPT minimizes average completion time, improving responsiveness without excessively delaying longer tasks.
This leads to production downtime, schedule inertia, and inefficient resource utilization.
The increasing complexity of Industry 4.0 manufacturing systems demands real-time, adaptive scheduling capable of responding instantly to unexpected events.

## Slide 5: How Others Have Approached This

## Slide 6
1. Heuristic and Rule-Based Methods
Methods like FIFO, SPT, EDD, and LPT are easy to apply and require minimal computation.
These rules focus only on local machine-level decisions, not overall production efficiency.
They often cause bottlenecks, idle times, and poor adaptability to dynamic shop floor changes.
Main limitation: They cannot optimize global objectives such as minimizing makespan or overall tardiness.
Source: A. K. Kaban, Z. Othman and D. S. Rohmah, “Comparison of dispatching rules in job-shop scheduling problem using simulation: A case study,” Int. J. Simul. Model., vol. 11, no. 3, pp. 129-140, Sept. 2012, doi:10.2507/IJSIMM11(3)2.201

## Slide 7
2. Meta-Heuristic Algorithms
Techniques like Particle Swarm Optimization (PSO) and Ant Colony Optimization (ACO) explore large solution spaces to find near-optimal schedules.
They provide high-quality solutions, outperforming simple heuristics in complex scheduling scenarios.
However, these methods require many iterations, making them computationally expensive and slow for real-time use.
In dynamic or fast-changing environments, their long re-optimization time limits adaptability and practicality.
Source :M. Ventresca and B. M. Ombuki, “Ant Colony Optimization for Job Shop Scheduling Problem,” Tech. Rep. CS-04-04, Department of Computer Science, Brock University, St. Catharines, Ontario, Canada, Feb. 2004.

## Slide 8: Comparison to Related Work
Method | Pros | Cons | Our Choice
FIFO | Simple, easy to implement, very fast decisions | Ignores job priorities and processing times → poor overall performance | Used as baseline for comparison
SPT (Shortest Processing Time) | Reduces average completion time; efficient for small systems | Myopic — may delay long or urgent jobs | Used as secondary baseline
Ant Colony Optimization | Finds near-optimal solutions for complex problems | Slow, high computation cost → not suitable for real-time | Replaced by learning-based approach
Deep Reinforcement Learning | Adaptive, handles dynamic environments, fast inference after training | Needs long training and careful tuning | Best balance of performance and adaptability

## Slide 9: Baseline Methods: Heuristics
What are Heuristics?
Heuristics are efficient "rules of thumb" for problem-solving. They trade guaranteed optimality for speed, providing fast, "good enough" solutions.
In scheduling, these are dispatching rules that instantly select the next job for a free machine based on a simple, pre-defined property
Classification of Methods
Simple Dispatching Rules:
Static, low-computation rules. They are very fast but not adaptive. (e.g., FIFO, SPT)
Metaheuristics
More complex, "smarter" search algorithms. They find better solutions but are slower to run. (e.g., Ant Colony)

## Slide 10: The Deep RL Advantage
Adaptive Learning
Unlike static rules (FIFO/SPT), a Deep RL agent learns an optimal *policy* from experience. It adapts its strategy to the current, complex state of the *entire* shop
Far-Sighted Strategy
Heuristics are myopic(e.g., SPT only looks at the next step). Deep RL learns to maximize long-term rewards (the final makespan), not just the immediate, greedy choice.
Real-Time & Generalized
Metaheuristics (like ACO) must re-run a slow search for each new problem. A trained Deep RL agent generalizes and provides an instant, high-quality decision for any state.
Source: da Cunha and de Madureira, "A Multi-Agent ReinforcementLearning Approach...," Sustainability, 2023. Available: https://www.mdpi.com/2071-1050/15/10/8262

## Slide 11
Python Environment
Developed a robust, discrete-event simulation environment for the job shop scheduling problem (JSSP).
Baseline Heuristics
Implemented and benchmarked standard dispatching rules: First-In, First-Out (FIFO) and Shortest Processing Time (STO).
Completed Milestones
Baseline Results
SPT (179 Jobs, 6.9k Tardiness) vastly outperforms FIFO (165 Jobs, 21.8k Tardiness). SPT's high throughput and low tardiness make it the superior baseline for our DRL agent to beat.

## Slide 12: The image compares FIFO and SPT scheduling methods, showing that SPT (Shortest Processing Time) delivers superior performance by completing more jobs (179 vs. 165) and greatly reducing total tardiness (6,996.10 vs. 21,864.55) while maintaining the same makespan and machine configuration, proving it to be a much more efficient and deadline-focused scheduling strategy.
Baseline Results:
Metric | FIFO (First-In, First-Out) | SPT (Shortest Processing Time) | Interpretation
1. Number of Jobs Completed | 165 | 179 | SPT is significantly better at throughput.
2. Total Tardiness | 21864.55 | 6996.1 | SPT is dramatically better at meeting deadlines.(ATUs)
3. Makespan (Sim Time) | 1000 | 1000 | Simulation run time is constant.(ATUs)
4. Machines Used | 3 | 3 | Configuration is identical.

## Slide 13: Future Work and Next Steps
Develop and integrate
Deep Reinforcement Learning
Implement
Metaheuristic Benchmarks: Implement Ant Colony Optimization (ACO)and Swarm Intelligence as an advanced, non-learning-based comparison method.
Perform
Comparative Analysis: Perform a comprehensive benchmark of all methods (Heuristics, Deep RL, Metaheuristics) to minimize makespan.

## Slide 14: Project Timeline
16 Oct. 2025
P1: Proposal & MVP
6 Nov. 2025
P2: Core Logic & Baselines
27 Nov. 2025
P3: Full Deep RL Agent and Metaheuristic methods
18 Dec. 2025
P4: Results Analysis
15 Jan. 2026
P5: Final Report

## Slide 15: THANK YOU